## Slide 1: ECE411 - Practicum T05 – Electronic Compass
Cody Gabriel
Benjamin Huntsman
John Maseda
Michael Walton

## Slide 2: Need
Land Navigation

## Slide 3: Motivation

## Slide 4: Objective
Our objective is design, build, and test a working digital compass prototype.
The design will incorporate:
  8-bit microcontroller as a processing unit
  magnetometer as an input sensor
  an LCD display as an output

## Slide 5: Alternatives
Many modern alternatives exist
  Analog compass
  Smartphone apps
  Handheld GPS devices

## Slide 6: Requirements (Course)
The project must:
Have one or more inputs or sensors
Have one or more outputs or transducers
Have one or more processing module
Use a 2-layer PCB
Use components that can be hand soldered or easily soldered in a crude reflow oven

## Slide 7: Requirements (Engineering)
The system should:
Be accurate to within 5° of true orientation
Have a switch to power on the device and be ready within a short period of time
Display on a LCD a heading either with a compass face or with letters (“NNW”) as well as a numerical value in degrees
Be prepared for software updates
[backlight??]

## Slide 8: Approach: Project Selection
A list of four possible projects were considered
Electronic Compass
Bicycle brake light/blinker system
Ironman Repulsor weapon
Homemade oscilloscope

## Slide 9: Approach: Initial Design
Major components selection
  μC: ATmega32u4
  Magnetometer/Accelerometer: LSM303DLH
  LCD: Nokia 5110
  PMIC: LTC4067
Research major components; understanding setup and operation
Order development boards from SparkFun for initial prototyping

## Slide 10: Approach: Schematic, Layout, & IDE
Application notes for the major components were considered
Decided to only implement μC and PMIC on manufactured board; LCD and magnetometer dev-boards connected via header pins
EAGLE CAD software used for schematic and layout
[IDE used for coding]

## Slide 11: Approach: Construction
The board layout was sent to OSH Park for fabrication
Two of our major components, Atmega32u4 and LTC4067 came in packages that were not hand solder-able
The ATmega32u4 chip that we used came in a QFN package, and the LTC4067 was in a DFN package
Due to the components that could not be soldered by hand, the reflow oven in the EPL was used for construction

## Slide 12: Design: Power Management

## Slide 13: Design: Microcontroller

## Slide 14: Design: Coding

## Slide 15: Implementation

## Slide 16: IP/Prior Work

## Slide 17: Testing

## Slide 18: Results

## Slide 19: Ben’s Contributions

## Slide 20: Michael’s Contributions

## Slide 21: John’s Contributions

## Slide 22: Cody’s Contributions

## Slide 23: Ben’s Lessons Learned

## Slide 24: Michael’s Lessons Learned

## Slide 25: John’s Lessons Learned

## Slide 26: Cody’s Lessons Learned