## Slide 1: ECE411 - Practicum T05 – Electronic Compass
Cody Gabriel
Benjamin Huntsman
John Maseda
Michael Walton

## Slide 2: Need
Land Navigation Human Calibration
Robot needs compass input
Project required for Practicum

## Slide 3: Motivation
The value is in the USB interface for Robot
Alternative compass solutions are analog or phone based with the primary user being Human.
Provides something that was not accessible at relatively low cost before.

## Slide 4: Objective
Our objective is design, build, and test a working digital compass prototype.
The design will incorporate:
  8-bit microcontroller as a processing unit
  magnetometer as an input sensor
  an LCD display as an output

## Slide 5: Alternatives
There are no COTS alternatives for the Robotic compass that are financially feasible.
Many modern alternatives exist for basic land navigation.
  Analog compass
  Smartphone apps
  Handheld GPS devices

## Slide 6: Requirements (Course)
The project must:
Have one or more inputs or sensors
Have one or more outputs or transducers
Have one or more processing module
Use a 2-layer PCB
Use components that can be hand soldered or easily soldered in a crude reflow oven

## Slide 7: Requirements (Engineering)
The system should:
Be accurate to within 5° of true orientation
Have a switch to power on the device and be ready within a short period of time
Display on a LCD a heading either with a compass face or with letters (“NNW”) as well as a numerical value in degrees
Be prepared for software updates
[backlight??]

## Slide 8: Approach: Project Selection
A list of four possible projects were considered:
Electronic Compass
Bicycle brake light/blinker system
Ironman Repulsor Weapon
Homemade oscilloscope

## Slide 9: Approach: Initial Design
Major components selection ($$)
  μC: ATmega32u4
  Magnetometer/Accelerometer: LSM303DLH
  LCD: Nokia 5110
  PMIC: LTC4067
Research major components; understanding setup and operation
Order development boards from SparkFun for initial prototyping

## Slide 10: Approach: Schematic, Layout, & IDE
Application notes for the major components were considered
Decided to only implement μC and PMIC on manufactured board; LCD and magnetometer dev-boards connected via header pins
EAGLE CAD software used for schematic and layout
[IDE used for coding]

## Slide 11: Approach: Construction
The board layout was sent to OSH Park for fabrication
Two of our major components, Atmega32u4 and LTC4067 came in packages that were not hand solder-able
The ATmega32u4 chip that we used came in a QFN package, and the LTC4067 was in a DFN package
Due to the components that could not be soldered by hand, the reflow oven in the EPL was used for construction

## Slide 12: Design: Power Management

## Slide 13: Design: Microcontroller

## Slide 14: Design: Coding

## Slide 15: Implementation
Board Layout: Eagle CAD Implemented
  Pin 1 Convention top left
  Caps as close as possible to ICs
  μC centered for space management
  Large power lines
  Signal Lines Rx, Tx same length
  LCD header centric
  Test points and vias for all GPIOs (modifiable)
  Magnetometer headers “Isolated” from noise

## Slide 16: IP/Prior Work
We utilized the LCD and Magnetometer Development Boards.
Implementing these COTS Items cost an extra 10$ per board, and added design, and implementation constraints.
Saving the time and effort of integrating these components.

## Slide 17: Testing

## Slide 18: Results

## Slide 19: Ben’s Contributions

## Slide 20: Michael’s Contributions

## Slide 21: John’s Contributions
Schematic Design: Initial layout, editing, revising, updating.
Layout: stack design, part placement, layer design, routing, organization, revising updating.
Implementation: oven soldering, hand soldering, assembly
Test:
Documentation:

## Slide 22: Cody’s Contributions

## Slide 23: Ben’s Lessons Learned

## Slide 24: Michael’s Lessons Learned

## Slide 25: John’s Lessons Learned
Getting started early sets up the team for success.
Problems will occur preparing for them is possible.
When it is not possible to prepare for a problem grace is required to deal with it.
Eagle Cad is a good free program.
Bulk board orders are cheaper
The EPL is an awesome but very small place to be

## Slide 26: Cody’s Lessons Learned