## Slide 1: ECE411 - Practicum T05 – Electronic Compass
Cody Gabriel
Benjamin Huntsman
John Maseda
Michael Walton

## Slide 2: Needs
Land Navigation Human Calibration
Robot needs compass input
Project required for Practicum

## Slide 3: Motivation
The value is in the USB interface for Robot
Alternative compass solutions are analog or phone based with the primary user being Human.
Provides something that was not accessible at relatively low cost before.

## Slide 4: Objective
Our objective is design, build, and test a working digital compass prototype.
The design will incorporate:
  8-bit microcontroller as a processing unit
  magnetometer as an input sensor
  an LCD display as an output

## Slide 5: Alternatives
There are no COTS alternatives for the Robotic compass that are financially feasible.
Many modern alternatives exist for basic land navigation.
  Analog compass
  Smartphone apps
  Handheld GPS devices

## Slide 6: Requirements (Course)
The project must:
Have one or more inputs or sensors
Have one or more outputs or transducers
Have one or more processing module
Use a 2-layer PCB
Use components that can be hand soldered or easily soldered in a crude reflow oven

## Slide 7: Requirements (Engineering)
The system should:
Be accurate to within 5° of true orientation
Have a switch to power on the device and be ready within a short period of time
Output on a display a heading either with a compass face or with letters (i.e. “NNW”) as well as a numerical value in degrees
Be prepared for software updates
Display must have a backlight for use in the dark

## Slide 8: Approach: Project Selection
A list of four possible projects were considered:
  Electronic Compass
  Bicycle brake light/blinker system
  Ironman Repulsor Weapon
  Homemade oscilloscope

## Slide 9: Approach: Initial Design
Major components selection ($$)
  μC: ATmega32u4
  Magnetometer/Accelerometer: LSM303DLH
  LCD: Nokia 5110
  PMIC: LTC4067
Research major components; understanding setup and operation
Order development boards from SparkFun for initial prototyping
Defining project requirements

## Slide 10: Approach: Schematic, Layout, & IDE
Application notes for the major components were considered
Decided to only implement μC and PMIC on manufactured board; LCD and magnetometer dev-boards connected via header pins
EAGLE CAD software used for schematic and layout
AVRdude for coding

## Slide 11: Approach: Construction
The board layout was sent to OSH Park for fabrication using their design rules
Two of our major components, Atmega32u4 and LTC4067 came in packages that were not hand solder-able
The ATmega32u4 chip that we used came in a QFN package, and the LTC4067 was in a DFN package
Due to the components that could not be soldered by hand, the reflow oven in the EPL was used for construction

## Slide 12: Design: System level 0

## Slide 13: Design: level 1

## Slide 14: Design: Power Management

## Slide 15: Design: Microcontroller

## Slide 16: Design: LCD

## Slide 17: Design: Coding

## Slide 18: Implementation
Board Layout: Eagle CAD Implemented
  Pin 1 Convention top left
  Caps as close as possible to ICs
  μC centered for space management
  Large power lines
  Signal Lines Rx, Tx same length
  LCD header centric
  Test points and vias for all GPIOs (modifiable)
  Magnetometer headers “Isolated” from noise

## Slide 19: IP/Prior Work
We utilized the LCD and Magnetometer Development Boards.
Implementing these COTS Items cost an extra $10 per board, and added design, and implementation constraints.
Saving the time and effort of integrating these components.

## Slide 20: Testing
PMIC:
  Use implemented test points for appropriate DC values
  Charge a battery and test its voltage ensuring that PMIC stops charging at correct voltage
  Check supply voltages to daughterboards
Microcontroller:
  Connect via USB
  GPIO’s used for switching power on to LCD and sensor easily verified using a multimeter
  Calibration verified using known working compass

## Slide 21: Testing
LCD:
  Check DC inputs
  View data signals with MSO through test points
  Visually verify text output
Magnetometer/Accelerometer
  Check DC inputs
  View data signals with MSO through test points
  Verify output by comparison of values on LCD to known working compass

## Slide 22: Results

## Slide 23: Ben’s Contributions

## Slide 24: Michael’s Contributions

## Slide 25: John’s Contributions
Schematic Design: Initial layout, editing, revising, updating.
Layout: stack design, part placement, layer design, routing, organization, revising updating.
Implementation: oven soldering, hand soldering, assembly
Test:
Documentation:

## Slide 26: Cody’s Contributions
Initial Design: PMIC selection
Schematic: adhered to application notes for USB battery charging and C busses, designed GPIO enabled transistor switches, minor parts selection
Parts order and tracking
Major contributor to group homework assignments and documentation
Testing:

## Slide 27: Ben’s Lessons Learned

## Slide 28: Michael’s Lessons Learned

## Slide 29: John’s Lessons Learned
Getting started early sets up the team for success.
Problems will occur preparing for them is possible.
When it is not possible to prepare for a problem grace is required to deal with it.
Eagle Cad is a good free program.
Bulk board orders are cheaper
The EPL is an awesome but very small place to be

## Slide 30: Cody’s Lessons Learned
Professional grade design and construction
Constant communication is key to success
Step up when the team needs you to
Verify all parts are ordered more than once
Don’t be complacent!

## Slide 31: The end